### MWA beam software standalone version ( updated on 2018-05-28 , by Marcin Sokolowski)
- Requirements :
  - python - standard python can be used, but if does not work then possibly this can be useful:
    - anaconda - might be an easy way to have many packages installed:
      https://www.continuum.io/downloads#linux
    - Installation : bash ./Anaconda2-4.4.0-Linux-x86_64.sh
  - I needed to install these two extra packages on the clean environment :
    - pip install ephem
    - pip install pyfits

### Generation of beam for a given fits files

  - Script : make_beam_test.py
    - Description :
      Generates beam images (fits files) for a given sky image
    - Parameters :
      In order to correctly generate beam model the following parameters are required :
- FITS file with sky image for which the beam model is generatd (option -f or --filename), frequency (options --freq_mhz or –freq_cc), beamformer delays (from metafits file, list of delays or MWA gridpoint) and time as observation id (option --obsid) or can be derrived from metafits file name (option --metafits).
      - -f or --filename FITS.fits : fits file for which beam model is generated (in the same resolution)
      - -m or --metafits : metafits file containg META data for this observation (beamformer delays are read from there in particular). In order to correctly generate beam beamformer delays must be provided in any of the three possible ways (--metafits, --delays or --gridpoint).
      - --beamformer or -d or --delays : beamformer delays provided in the command line parameter as a list , for example : -b 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6
      - -g or --gridpoint : provides MWA gridpoint number (also called sweet spot which also defines beamformer delays). List of MWA gridpoints can be found in files mwa_sweet_spots.py or MWA_sweet_spot_gridpoints.csv.
      - --model : which beam model to use, 2014 – oldest analytic model, 2015 – average embedded element (called AEE or advanced) model and 2016 (Full Embedded Element or FEE) model. Default is 2016 model (the newest and the most advanced).
      - --jones : generates Jones matrices (not just power beam)
      - --freq_cc – frequency coarse channel ( multiply by 1.28 to get MHz).
      - --freq_mhz – frequnecy in MHz
      - -o / --obsid – which is GPS time of the observation start provides time of the observation
      - Examples :
        - Using MWA metafits file which provides actual beamformer delays as used during the observation:
    - python make_beam_test.py -f 2456603.366393_img_200.335MHz_chan000of032_cal001_peel_000_000_t0000XX.fits --model=2016 --freq_mhz=203.51 -m 1067806072.metafits
        The metafits file can be downloaded using command:
      wget http://mwa-metadata01.pawsey.org.au/metadata/fits/?obs_id= 1067806072 -O 1067806072.metafits
        - Using beamformer delays as parameters:
      python make_beam_test.py -f wsclean_1067806072-0002-XX-dirty.fits -d 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6 -v --model=2016
        - Using metafits file :
          python make_beam_test.py -f wsclean_1067806072-0002-XX-dirty.fits --metafits 1067806072.metafits -v --model=2016

        - Using gridpoint number, which defines MWA delays (as in mwa_sweet_spots.py) :
    - python make_beam_test.py -f wsclean_1067806072-0002-XX-dirty.fits -g 11 -v --model=2016
        - Other examples :
      python make_beam_test.py -f 2456603.366393_img_200.335MHz_chan000of032_cal001_peel_000_000_t0000XX.fits -g 11 -v --model=2016 --obsid=1067806072 --freq_mhz=203.52

    python make_beam_test.py -f 2456603.366393_img_200.335MHz_chan000of032_cal001_peel_000_000_t0000XX.fits -d 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6 -v --model=2016 --obsid=1067806072 --freq_mhz=203.51

### Beam correction of images to generate Stokes images
  - Script beam_correct_image.py
    - Description :
      Beam corrects instrumental images in (four expected XX,YY,XY and XYi – as coming out of WSCLEAN or RTS) and calculates Stokes images (I,Q,U,V)
    - Parameters :
      Similar parameters are required to correctly beam correct instrumental polarisation images and obtain Stokes images :
- FITS file with sky image for which the beam model is generatd (option -f or --filename), frequency (options --freq_mhz or –freq_cc), beamformer delays (from metafits file, list of delays or MWA gridpoint) and time as observation id (option --obsid) or can be derrived from metafits file name (option --metafits).
  WARNING : --metafits not yet implemented
      - --xx_file , --yy_file, --xy_file, --xyi_file – provide names of FITS files with XX, YY, XY and XYi images.
      - --out_basename – basename (prefix) for the output files names, then _I, _Q, -U and -V are added to output filenames
      - TO BE IMPLEMENTED : -m or --metafits : metafits file containg META data for this observation (beamformer delays are read from there in particular). In order to correctly generate beam beamformer delays must be provided in any of the three possible ways (--metafits, --delays or --gridpoint).
      - --beamformer or -b or --delays : beamformer delays provided in the command line parameter as a list , for example : -b 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6
      - -g or --gridpoint : provides MWA gridpoint number (also called sweet spot which also defines beamformer delays). List of MWA gridpoints can be found in files mwa_sweet_spots.py or MWA_sweet_spot_gridpoints.csv.
      - --model : which beam model to use, 2014 – oldest analytic model, 2015 – average embedded element (called AEE or advanced) model and 2016 (Full Embedded Element or FEE) model. Default is 2016 model (the newest and the most advanced).
      - --freq_mhz – frequnecy in MHz
      - -o / --obsid – which is GPS time of the observation start provides time of the observation
      - --h5file – full path to HDF5 file with the full embedded element beam model (default is local file MWA_embedded_element_pattern_V02.h5)
      - --wsclean – if XX,YY,XY,XYi images come from WSCLEAN software
      - --rts – if images are from Real-Time System (RTS). WARNING : WSCLEAN and RTS software are known to follow different sign convention thus it is important to provide information on the software used to obtain correct sign values.
    - Using beamformer delays passed as parameter ( -b 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6 ) :
      python ./beam_correct_image.py --xx_file=wsclean_1067806072-0002-XX-dirty.fits --yy_file=wsclean_1067806072-0002-YY-dirty.fits --xy_file=wsclean_1067806072-0002-XY-dirty.fits --xyi_file=wsclean_1067806072-0002-XYi-dirty.fits -b 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6 --model=2016
    - Using gridpoint number (-g 11) which defines the delays :
      python ./beam_correct_image.py --xx_file=wsclean_1067806072-0002-XX-dirty.fits --yy_file=wsclean_1067806072-0002-YY-dirty.fits --xy_file=wsclean_1067806072-0002-XY-dirty.fits --xyi_file=wsclean_1067806072-0002-XYi-dirty.fits -g 11 --model=2016
    - Using analytic model :
      python ./beam_correct_image.py --xx_file=wsclean_1067806072-0002-XX-dirty.fits --yy_file=wsclean_1067806072-0002-YY-dirty.fits --xy_file=wsclean_1067806072-0002-XY-dirty.fits --xyi_file=wsclean_1067806072-0002-XYi-dirty.fits --model=analytic

### Sensitivity calculations
  - Sensitivity calculation (will also be provided as a webservice) uses script mwa_sensitivity.py :
    - Description :
      script calculates MWA sensitivity for specific observing parameters and time. It calcualtes SEFD and noise expected on images of a specified integration time (default 120 seconds) and bandwidth (default 1.28 MHz). The last lines of the standard output contain this information (“Noise expected on XX images”).
    - On-line prototype version is being developed, but currently it is not available to external users.
    - Parameters:
      Similar parameters are required to correctly beam correct instrumental polarisation images and obtain Stokes images :
- FITS file with sky image for which the beam model is generatd (option -f or --filename), frequency (options --freq_mhz or –freq_cc), beamformer delays (from metafits file, list of delays or MWA gridpoint) and time as observation id (option --obsid) or can be derrived from metafits file name (option --metafits).
      - -m or --metafits : metafits file containg META data for this observation (beamformer delays are read from there in particular). In order to correctly generate beam beamformer delays must be provided in any of the three possible ways (--metafits, --delays or --gridpoint).
      - --beamformer or -b or --delays : beamformer delays provided in the command line parameter as a list , for example : -b 0,0,0,0,2,2,2,2,4,4,4,4,6,6,6,6
      - --gridpoint : provides MWA gridpoint number (also called sweet spot which also defines beamformer delays). List of MWA gridpoints can be found in files mwa_sweet_spots.py or MWA_sweet_spot_gridpoints.csv.
      - --model : which beam model to use, 2014 – oldest analytic model, 2015 – average embedded element (called AEE or advanced) model and 2016 (Full Embedded Element or FEE) model. Default is 2016 model (the newest and the most advanced).
      - --jones : generates Jones matrices (not just power beam)
      - -c or --channel or --freq_cc – frequency coarse channel ( multiply by 1.28 to get MHz).
      - --freq_mhz or -f or --frequency – frequnecy in MHz
      - --gps / --obsid – which is GPS time of the observation start provides time of the observation
      - --datetimestring – UTC time of the observation
      - -D or --date : UT date of the observation
      - -t or --time : UT time of the observation
      - --plottype / -p : plotting option. Type of plot: all, beam, sky, beamsky, beamsky_scaled. It allows to generate beams for any pointing (without providing FITS file with sky image as make_beam_test.py does).
      - --title : plot title
      - --ext or -e : plot file extention/format (default png)
      - --no_zenith_norm or -n : turns off zenith normalization of the beam model (default)
      - --size : resolution of the used beam model
      - --dir : directory where generated beam model files are saved
      - --pointing_za_deg – zenith angle where sensitivity is calculated [in decimal degrees] alternatively --pointing_elev_deg can be used to specify elevation [in decimal degrees ]
      - --pointing_az_deg – azimuth angle where sensitivity is calculated [in decimal degrees]
      - --t_rcv : value of receiver temperature in Kelvin [default 0], overwrites option –trcv_type
      - --trcv_type : which receiver temperature measurement is to be used [default is the one based on EDA drift scan and HASLAM map fit], can be overwritten by the option –t_rcv
      - -x / --outsens_file : name of output sensitivity file
      - NOT YET IMPLEMENTED : --add_sources : if add sources to the generated beam/sky image
      - -v or --verbose : to generate more debugging output
    - Examples :
      - Test case obsid = 1190024128 with expected results :
        - wget http://mwa-metadata01.pawsey.org.au/metadata/fits/?obs_id=1190024128 -O 1190024128.metafits
        - python ./mwa_sensitivity.py -c 69,93,121,145,169 -p all --metafits=1190024128.metafits -m full_EE --pointing_az_deg=328.309328 --pointing_za_deg=36.246219 --outsens_file=test_HerA_db > output_db 2>&1
        - or with option --gridpoint=80
        - Expected results in test_HerA_db_XX.txt :
88.32000000 0.00564678 3681.76 20.79009433 0.00000000
119.04000000 0.01249623 1463.97 18.29416600 0.00000000
154.88000000 0.02358699 709.51 16.73515452 0.00000000
185.60000000 0.02923237 446.79 13.06087541 0.00000000
216.32000000 0.02398064 326.35 7.82617055 0.00000000
        - Expected noise on XX and YY images (in output_db file) :
Noise expected on XX images = 0.0728 Jy
Noise expected on YY images = 0.0656 Jy
      - At zenith gridpoint ( --gridpoint=0) and 5 degrees off zenith (--pointing_za_deg 5 --pointing_az_deg 0), frequency 185.6 MHz, integration time 120 sec, using 60 antennas (--antnum=60), also generates beam images (option -p all) at GPS time 1193567480 ( -g 1193567480) :
        python ./mwa_sensitivity.py -f 185.6 --model 2016 --pointing_za_deg 5 --pointing_az_deg 0 --antnum=60 --inttime=120 -p all --gridpoint=0 -g 1193567480

### C/C++ implementations

- C/C++ implementations of the 2016 MWA beam model :
  - Real-time System (RTS) C implementation, for details please contact Bart Pindor (not sure if this is in the main version or a test branch in git)
  - Andre's (C++ version). In calibrate and beam (option -2016) can also use the 2016 model if it is enabled on compilation level or via parameters.